## Slide 1
Scope: replication of the static optimizers, NSGA-II parameters, and SLA constraints.
Reference: Agoran: An Agentic Open Marketplace for 6G RAN Automation
Multi-objective optimization is used when improving one objective may degrade another. NSGA-II helps identify tradeoffs among throughput, latency, cost
NSGA-II Baseline
NSGA-II (Non-Dominated Sorting Genetic Algorithm II)

## Slide 2
Global Resource Limits
Resource | Max Limit
Bandwidth (MHz) | 300.0
Compute (units) | 500.0
Power (W) | 100.0
Storage MB | 300.0

## Slide 3
SLA Constraints
Slice | Throughput Min (Mbps) | Latency Max (ms) | Cost Max (EUR)
eMBB | 60.0 | 10.0 | 200.0
URLLC | 5.0 | 2.0 | 200.0
mMTC | 20.0 | 10.0 | 30.0

## Slide 4
KPIs of Best Solution
Slice | Throughput (Mbps) | Latency (ms) | Cost EUR (EUR) | Energy (W)
eMBB | 730.6518 | 0.03286 | 10.0226 | 11.1520
URLLC | 212.4432 | 0.03395 | 38.24082 | 1.4455
mMTC | 415.9288 | 0.1155 | 4.0881 | 58.8746

## Slide 5: Front 0 Pareto Solutions: Slice KPIs
ID | Slice | Throughput (Mbps) | Latency (ms) | Cost (EUR) | Energy (W)
2 | eMBB | 559.3714 | 0.0429 | 1.6172 | 60.3036
 | URLLC | 344.6937 | 0.0209 | 2.2034 | 1.4455
 | mMTC | 415.9288 | 0.1155 | 11.7710 | 31.7038
3 | eMBB | 454.9465 | 0.0528 | 5.1339 | 2.0864
 | URLLC | 206.6346 | 0.0349 | 2.2034 | 1.4455
 | mMTC | 209.5738 | 0.2296 | 12.9685 | 2.6128
4 | eMBB | 523.1036 | 0.0459 | 1.6172 | 60.3036
 | URLLC | 344.6937 | 0.0209 | 59.0540 | 48.8602
 | mMTC | 415.9288 | 0.1156 | 0.7999 | 12.8241

## Slide 6: Experimental Setup
The NSGA-II configuration used in this implementation includes:
- num_generations = 100
- sol_per_pop = 60
- num_parents_mating = 10
- parent_selection_type = "nsga2"
- mutation_percent_genes = 10
- crossover_probability = 0.1
- pygad == 3.2.0